## Slide 1
Addendum to the previous supplementary material:
De Winter, J. C. F., Hu, J., & Petermeijer, S. (2022). Ipsilateral and contralateral warnings: Effects on decision-making and eye movements in near-collision scenarios. [Dataset]. https://doi.org/10.4121/19524448
, belonging to the following paper:
De Winter, J., Hu, J., & Petermeijer, B. (2022). Ipsilateral and contralateral warnings: Effects on decision-making and eye movements in near-collision scenarios. Journal on Multimodal User Interfaces. https://doi.org/10.1007/s12193-022-00390-6
In the published paper, only ‘completed’ fixations were taken into consideration. For example, if a trial lasted 1.0 seconds, the last fixation started at 0.9 seconds, and the fixation did not end before the trial ended, the fixation was not taken into consideration in the analysis. We recently updated the fixation filter Eyelink (see FixationFilterEyelink1000v106.m available at https://doi.org/https://doi.org/10.4121/21816081) to also extract non-completed fixations, combined with various other improvements (improvement of ‘edge cases’, such as trials with 0 or 1 fixations, better annotation, etc).
We reran the code, and the updated results are shown on the next slides.
This updated supplementary material contains a MATLAB script (readeyeJan2023.m) that processes the eye-tracking data and a MATLAB script (responsesJan2023.m) that produces the figures of the paper. The original readme.txt is available at https://doi.org/10.4121/19524448

## Slide 2: Figure 7: top Area of interest of first fixation, relative to the total number of trials in which eye-tracking data were available
Updated
“The location of the first, second, and third fixations (excluding fixations on the dashboard) was determined from the mean of the coordinates during the fixation.”
“Figure 7 shows the distribution of where the participants’ first fixation landed. It can be seen that the traffic situation (i.e., time budget and escape direction) affected the distribution of fixations, whereas the audio type (i.e., Danger, Go, Baseline) did not have a distinct influence. More specifically, in the 1-s videos, participants generally first looked at the road center (red bars) for all audio types; in the center, there was a stranded car, which was presumably the most salient stimulus for the critical 1-s time budget. Additionally, participants were more likely to place their first fixation on the hazard side (i.e., green bars relative to gray bars) than on the escape side for all audio types. This effect was especially strong with the 3-s time budgets in which the overtaking car was relatively close at the start of the video.”
Published paper

## Slide 3: Figure 7: middle Area of interest of second fixation, relative to the total number of trials in which eye-tracking data were available
Published paper
“Figure 7 further shows the area-of-interest distribution of the second and third fixations. It can be seen that compared to the first fixation, attention was attracted away from the center road towards other areas, including the center mirror. For the 1-s videos, a second and third fixation were available in only about 35% and 15% of the trials, respectively, i.e., most participants had responded before placing their second fixation. No consistent differences between the three audio types are apparent.”
The yellow text should, more accurately, say: “For the 1-s videos, a second and third fixation were available in only about 75% and 35% of the trials, respectively”
Updated

## Slide 4: Figure 7: bottom Area of interest of third fixation, relative to the total number of trials in which eye-tracking data were available
Published paper
Updated
“Figure 7 further shows the area-of-interest distribution of the second and third fixations. It can be seen that compared to the first fixation, attention was attracted away from the center road towards other areas, including the center mirror. For the 1-s videos, a second and third fixation were available in only about 35% and 15% of the trials, respectively, i.e., most participants had responded before placing their second fixation. No consistent differences between the three audio types are apparent.”
The yellow text should, more accurately, say: “For the 1-s videos, a second and third fixation were available in only about 75% and 35% of the trials, respectively”

## Slide 5: Figure 8 Mean first fixation times with 95% confidence intervals
“Finally, Figure 8 further shows the moment of the first fixation; it can be seen that participants placed their first fixation about 200–250 ms after the trial started. In other words, the first fixation occurred well before the typical response time of 800 ms in the shortest time-budget condition.”
Published paper
Updated